## Slide 1: Arduino
Muhammad Rizwan

## Slide 2: Micro-Controller
A single chip Computer
Has……
  CPU
  RAM
  EEPROM
  I/O in form of pins
  Peripherals (Timer , Communication modes , ADC etc)

## Slide 3: ????
Suppose we want to make a Line following Robot
What do we do ?
Use a computer with 2.4 GHz Intel core i7 with 4 Gb RAM , 500 Gb Hard disk , 1 Gb Graphics Card ??

## Slide 4: Why not a Computer ?•
PC is a general purpose computer.
Can run thousand of software's
Microsoft ppt in which you are seeing this presentation
Games (NFS , AOE , Call of Duty)
Highly expensive

## Slide 5: Why MCU?
Small reflected by the word “MICRO”
Inexpensive
Ideal for doing repetitive tasks
Easy to use
Highly Efficient and fast

## Slide 6: Selecting a MCU
Two family of MCU extremely popular
  AVR
  PIC
The instructions are fed once in the form of a Hex file

## Slide 7: Microcontroller and Programmer

## Slide 8: What is an Arduino ?
Open Source electronic prototyping platform based on flexible easy to use hardware and software.

## Slide 9: Most popular Arduino Boards
Arduino Uno
Arduino Leonardo
Arduino Mega
Arduino Due
Arduino Micro
Arduino LilyPad
Arduino Yun

## Slide 10: What can it do?
Sensors ( to sense stuff )
  Push buttons, Touch pads.
  Thermistors (temperature)
  Ultrasound (proximity range finder)
Actuators ( to do stuff )
  Lights, LED’s
  Motors
  Speakers
  Displays (LCD)

## Slide 11: Shields and Supports
Ethernet Shield
Relay Shield
Proto Shield [Permanent]
Motor Shield
Can Bus Shield [on board diagnosis]
Joystick Shield Kit
GSM / GPRS Shield
Micro SD Shield

## Slide 12: Meet Arduino Uno

## Slide 13: Getting Started
Check out: http://arduino.cc/en/Guide/HomePage
  Download & install the Arduino environment (IDE)
  Connect the board to your computer via the USB cable
  If needed, install the drivers
  Launch the Arduino IDE
  Select your board
  Select your serial port
  Open the blink example
  Upload the program

## Slide 14: Bare minimum code
void setup() { // put your setup code here, to run once:
}
void loop() { // put your main code here, to run repeatedly:
}
setup : It is called only when the Arduino is powered on or reset. It is used to initialize variables and pin modes
loop : The loop functions runs continuously till the device is powered off. The main logic of the code goes here. Similar to while (1).

## Slide 15: PinMode
A pin on Arduino can be set as input or output by using pinMode function.
pinMode(13, OUTPUT); // sets pin 13 as output pin
pinMode(13, INPUT); // sets pin 13 as input pin

## Slide 16: Reading/writing digital values
digitalWrite(13, LOW); // Makes the output voltage on pin 13 , 0V
digitalWrite(13, HIGH); // Makes the output voltage on pin 13 , 5V
int buttonState = digitalRead(2); // reads the value of pin 2 in buttonState

## Slide 17: Analog to Digital Conversion
What is analog ?
It is continuous range of voltage values (not just 0 or 5V)
Why convert to digital ?
Because our microcontroller only understands digital.

## Slide 18: ADC in Arduino Uno

## Slide 19: ADC in Arduino
The Arduino Uno board contains 6 pins for ADC
10-bit analog to digital converter
This means that it will map input voltages between 0 and 5 volts into integer values between 0 and 1023

## Slide 20: Reading/Writing Analog Values
analogRead(A0); // used to read the analog value from the pin A0
analogWrite(2,128);

## Slide 21: Thanks.
Any Question?
?